## Slide 1
Drone-based mapping system generates 3D terrain models
Multi-View Geometry • Binocular Vision • Image Formation
Name: Cheredla Jasvina
Reg. No: 192324026
DSA0201 – Computer Vision with OpenCV

## Slide 2
From Drone Photos to 3D Terrain
1
Image Formation
Each camera shot converts 3D light from the terrain into a 2D pixel image.
→
2
Binocular / Stereo Vision
Two overlapping views from nearby drone positions give depth by disparity.
→
3
Multi-View Geometry
Many overlapping images across the flight path are combined to reconstruct full 3D terrain.
2

## Slide 3
A. Multi-View Geometry
Multi-view geometry studies how a single 3D scene projects onto multiple 2D images taken from different camera positions - exactly what happens as a drone flies over terrain, capturing overlapping photos.
Terrain surface
P (terrain point)
Cam 1
Cam 2
Cam 3
Camera pose estimation
Recovers each camera's position & orientation as the drone moves.
Epipolar geometry
Constrains where a point in one image can appear in another.
Triangulation
Intersects rays from 2+ views to compute the 3D coordinates of a terrain point.
Structure from Motion (SfM)
Combines all overlapping images into one consistent 3D point cloud.
4

## Slide 4
Multi-View Geometry in the Mapping Pipeline
1
Capture
Drone flies a grid pattern, taking overlapping photos (60–80% overlap).
›
2
Feature Matching
Common ground features (rocks, roads, corners) are matched across images.
›
3
Bundle Adjustment
Camera poses & 3D points are jointly refined to minimize reprojection error.
›
4
Dense Reconstruction
A dense 3D point cloud / mesh of the terrain is generated.
Result: A geometrically accurate 3D terrain model (digital surface/elevation model), built purely from the geometric relationships between many 2D drone images — the core output multi-view geometry makes possible.
5

## Slide 5
B. Binocular Vision
Binocular vision is the use of two viewpoints — like human eyes — to perceive depth. In drone mapping, two images taken from slightly different positions along the flight path form a stereo pair used to compute how far away each terrain point is.
Terrain point
Left view
Right view
baseline (b)
Depth Z ∝ (focal length × baseline) / disparity
•
Disparity
Difference in pixel position of the same point between the two images.
•
Baseline
Distance between the two camera (drone) positions when each photo was taken.
•
Depth from disparity
Larger disparity = closer object; smaller disparity = farther terrain.
7

## Slide 6
Binocular Vision in Drone Mapping
1
Stereo Pair Selection
Consecutive overlapping frames along the flight path act as the 'left' and 'right' eye.
2
Correspondence Matching
Matching pixels between the pair using feature descriptors (e.g., SIFT/ORB in OpenCV).
3
Disparity Map
A dense map of pixel shifts is computed for every matched point (cv2.StereoBM/SGBM).
4
Elevation Estimate
Disparity is converted to height/depth, giving a local terrain elevation estimate.
Why it matters for terrain mapping
Binocular (stereo) vision gives fast, localized depth for each pair of frames — useful for quick elevation checks — while multi-view geometry later fuses many such pairs across the whole flight into one consistent, globally accurate 3D terrain model.
8

## Slide 7
C. Image Formation -The Pinhole Camera Model
Image formation describes how light reflected from the 3D terrain passes through the drone's camera lens and is projected onto a 2D sensor, producing the pixel image used by all downstream vision steps.
Terrain object
Lens / aperture
Image sensor plane
Inverted image
f
Projection
3D world point P(X,Y,Z) maps to 2D image point p(x,y) through the lens center.
Focal length (f)
Distance from lens to sensor; controls scale/zoom of the projected image.
Sensor
Converts incoming light into pixel intensity values, forming the digital image.
10

## Slide 8
Image Formation - Camera Parameters
Two parameter sets fully describe image formation for a drone camera — and both are needed before multi-view geometry or stereo depth can be computed.
Intrinsic Parameters
Internal to the camera itself
•
Focal length
Determines image scale and field of view
•
Principal point
Where the optical axis meets the sensor
•
Pixel size / aspect
Converts physical units to pixel coordinates
•
Lens distortion
Radial/tangential warping to correct for
Extrinsic Parameters
Camera's position in the world
•
Rotation (R)
Orientation of the drone/camera at capture
•
Translation (t)
GPS/IMU position of the camera in 3D space
•
Changes every frame
Updated continuously as the drone flies
•
Feeds multi-view geometry
Poses link every image into one 3D model
11

## Slide 9
Putting It All Together
1
Image Formation
Turns raw light from the terrain into usable 2D pixel images (per photo).
2
Binocular Vision
Pairs of images estimate local depth/disparity between two nearby viewpoints.
3
Multi-View Geometry
Fuses all overlapping images and poses into one consistent 3D terrain model.